## Slide 1: EECS 370 Discussion
xkcd.com

## Slide 2: EECS 370 Discussion
Topics Today:
  ARM Addressing
    Endianness, Loading, and Storing Data
  Data Layout
    Struct Packing
  Control Flow
    Branches and PSR (Program Status Register)
  Conditional Assembly
    Predicated Assembly Instructions
  C to ARM Translation

## Slide 3: EECS 370 Discussion
ARM Addressing

## Slide 4: EECS 370 Discussion
ARM Addressing
Big-Endian means Big End First
Most Significant Byte (MSB) at first address in memory
In EECS370 we use Big-Endian
Applies to Bytes only!

## Slide 5: EECS 370 Discussion
ARM Addressing
Example:
sub r1, r1, #0x2
strh r1, [r2, #0x0]
ldrsb r2, [r2, #0x1]
ldrh r1, [r0, #0x1002]

## Slide 6: EECS 370 Discussion
Data Layout
Golden Rule
Start address of a variable is aligned based on the variable’s type
char – byte aligned
short – halfword aligned
int – word aligned
pointer – word aligned
double – two-word aligned
Structs
- start aligned based on alignment of largest member
- end padded to make overall size a multiple of largest member

## Slide 7: EECS 370 Discussion
Data Layout
Example:
  char a;
  char* b;
  short c;
  double* d;
  struct {
  int e;
  char f[10];
  } g;

## Slide 8: EECS 370 Discussion
Control Flow
ARM Registers:
16 total registers
R0 – R12: General Purpose
R13: Stack Pointer
R14: Link Register
R15: Program Counter  Dangerous!

## Slide 9: EECS 370 Discussion
Control Flow
Program Status Register (PSR):
Flags set by various assembly instructions
N – result is negative
Z – result is zero
C – result had a carry out of bit 31
V – result had an overflow

## Slide 10: EECS 370 Discussion
Control Flow
Branch Condition Codes based on PSR
  eq EQual Z == 1
  ne Not Equal Z == 0
  ge Greater than/Equal N == V
  lt Less Than N != V
  gt Greater Than Z == 0 && N == V
  le Less than/Equal Z == 1 || N != V
  cs unsigned higher/Same C == 1
  cc unsigned lower C == 0
  mi negative N == 1
  pl positive/Zero N == 0
  vs oVerflow Set V == 1
  vc no oVerflow Clear V == 0
  hi unsigned HIgher C == 1 && Z == 0
  ls unsigned Lower/Same C == 0 || Z == 1
  al any/Always

## Slide 11: EECS 370 Discussion
Conditional Assembly
Condition Codes can also be applied to other instructions
Example: Translate the following code
while (r0 != 0) {
if (r0 > 0) {
r0 = r0 – 1;
} else {
r0 = r0 + 1;
}
}

## Slide 12: EECS 370 Discussion
C to ARM Translation
Do some examples.
How to move 32-bit values into registers.