## Slide 1: EECS 370 Discussion
Sample Exam Questions

## Slide 2: EECS 370 Discussion
Not Really…
xkcd.com

## Slide 3: EECS 370 Discussion
Topics Today:
  Processor Components
  Single-Cycle Datapath
  Project 2
  Time for Questions

## Slide 4: EECS 370 Discussion

## Slide 5: EECS 370 Discussion
Processor Components
Control Blocks

## Slide 6: EECS 370 Discussion
Processor Components - Mux
Used to choose options
if (select == 0) {
OUT = IN1;
} else {
OUT = IN2;
}

## Slide 7: EECS 370 Discussion
Processor Components - Decoder
Allows an N-bit binary number to select one of 2N output lines
IN | OUT
000 | 00000001
001 | 00000010
010 | 00000100
011 | 00001000
100 | 00010000
101 | 00100000
110 | 01000000
111 | 10000000

## Slide 8: EECS 370 Discussion
Processor Components – ROM
Just a memory!
Address | Data
000 | 1001
001 | 0100
010 | 0010
011 | 1001
100 | 0010
101 | 0001
110 | 1000
111 | 0000

## Slide 9: EECS 370 Discussion
Processor Components – ROM

## Slide 10: EECS 370 Discussion
Processor Components – ROM

## Slide 11: EECS 370 Discussion
Processor Components
Mathematic Blocks

## Slide 12: EECS 370 Discussion
Processor Components – Sign Extension Unit
Increases the number of bits in a value
Adds 1s or 0s as appropriate

## Slide 13: EECS 370 Discussion
Processor Components – Adder
OUT = IN1 + IN2;
Is this a Half-Adder or Full-Adder?

## Slide 14: EECS 370 Discussion
Processor Components – ALU
Performs math operations
if (f == 0) {
OUT = IN1 + IN2;
} else {
OUT = IN1 ~& IN2;
}
EQ = (IN1 == IN2);

## Slide 15: EECS 370 Discussion
Processor Components
State Blocks

## Slide 16: EECS 370 Discussion
Processor Components – Registers
R_ADDR1
R_ADDR2
W_ADDR
W_DATA

## Slide 17: EECS 370 Discussion
Processor Components – Memory

## Slide 18: EECS 370 Discussion
Single Cycle Datapath

## Slide 19: EECS 370 Discussion

## Slide 20: EECS 370 Discussion
Single Cycle Datapath
Key Concept: Entire path executes in a single clock cycle
Fetch Instruction
Decode Instruction
Execute Instruction
Memory Access
Writeback Data
This limits the clock speed to slowest instruction

## Slide 21: EECS 370 Discussion
Single Cycle Datapath
Example: 5ns Reg Access, 10ns ALU Op, 20ns Mem Access
Inst | I-Mem Access | Read Register | ALU Operation | D-Mem Access | Write Register
add | ✔ | ✔ | ✔ |  | ✔
nand | ✔ | ✔ | ✔ |  | ✔
lw | ✔ | ✔ | ✔ | ✔ | ✔
sw | ✔ | ✔ | ✔ | ✔ | 
beq | ✔ | ✔ | ✔ |  | 
jalr | ✔ | ✔ |  |  | 
noop | ✔ |  |  |  | 
halt | ✔ |  |  |  | 

## Slide 22: EECS 370 Discussion
Project 2

## Slide 23: EECS 370 Discussion
Project 2
Suggested Register Convention
HIGHLY recommended you follow this
Register | Use
R0 | Value 0
R1 | Input N
R2 | Input R
R3 | Return Value
R4 | Local Variable
R5 | Stack Pointer
R6 | Temporary Value
R7 | Return Address

## Slide 24: EECS 370 Discussion
Exam Review Questions
?